## Slide 1
A Survey on State-of-the-Art Drowsiness Detection Techniques
Systematic review of behavioral, vehicular & physiological detection approaches
Ramzan, Khan, Awan, Ismail, Ilyas & Mahmood - IEEE Access, Vol. 7, 2019

## Slide 2
Overview & Scope
What this survey covers
• Problem Drowsiness / fatigue is a major cause of road accidents with serious safety implications.
• Goal Warn drowsy drivers in time to prevent deadly accidents.
• Approach Comprehensive analysis of existing driver drowsiness detection techniques (DDT).
• 3 categories Behavioral, vehicular and physiological parameter-based techniques.
• Classifiers Top supervised learning methods: SVM, HMM and CNN.
• Output Pros & cons, comparative study, frameworks and future research directions.
Key Stats from the Review
• 1,020 research papers in primary search • 105 selected by title • 74 after abstract screening • 41 papers as primary study Sources: IEEE Xplore, ACM, Springer, Google Scholar, IJCS, MDPI
2

## Slide 3
Introduction
Why drowsiness detection matters
• NHTSA report Drowsy driving causes ~100,000 accidents and 1,500+ deaths per year (US).
• Causes of fatigue Lack of sleep, long journeys, restlessness, alcohol, mental pressure, road rage.
• Impact Lack of alertness from the unconscious wake-to-sleep transition leads to serious accidents.
Motivation
Embedding automatic fatigue detection systems into vehicles can prevent deadly accidents by continuously analyzing the driver's attention level and alerting before a serious threat arises.
Why a survey?
Previous transportation systems cannot handle these hazards on roads; a systematic review classifies existing techniques, measures, tools and classification methods to identify research gaps.
3

## Slide 4
Research Methodology
Systematic review of drowsiness detection techniques
• Search string (Drows* OR Fatigu*) AND (Biological* OR Physiological* / Vehicle* / Behavioral* / Classif* / SVM* / CNN* / HMM*).
• Databases IEEE Xplore, ACM, Springer, Google Scholar, IJCS, MDPI.
• Quality checks Relevance to the research domain + publication in a well-reputed journal or conference.
Paper Selection Funnel
1,020 papers found ↓ title relevance 105 papers ↓ abstract screening 74 papers ↓ full-text study 41 primary studies selected
4

## Slide 5
Three Categories of Detection Techniques
Main architecture of drowsiness detection systems
1. Behavioral
Non-invasive camera + computer vision. Uses eye closure ratio (PERCLOS), blinking, head position, facial expressions, yawning. + No body contact - Affected by illumination & road conditions
2. Vehicular
Sensors on steering wheel, accelerator, brake. Uses lane-change patterns, speed variability, steering angle, grip force. + No driver instrumentation - Depends on weather & road geometry
3. Physiological
Monitors heart rate, pulse, breathing, temperature via EEG, ECG, PPG, HRV sensors. + Most accurate & reliable - Invasive; electrodes on the body
5

## Slide 6
Behavioral Parameter-Based Techniques
Eye, face & mouth analysis via computer vision
Technique | Approach | Result
Eye Tracking + Dynamic Template Matching [3] | HSI face detection, Sobel edge operator for eyes | 99.01% accuracy
Mouth & Yawning Analysis [4] | Mouth tracking + SVM classification of yawning | Better than geometric features
Facial Expressions [5] | Infrared light, background subtraction, template matching | Works with beard/glasses
Yawning Extraction [6] | SVM face region, CHT to find wide-open mouth | 98% accuracy
Eye Closure & Head Postures [7] | Viola-Jones + Wavelet network, head inclination | 80% accuracy
Eye Blink Detection [9] | Cascade classifiers, blink-rate below normal range | 90% efficiency
Eye Tracking (PERCLOS) [10] | AdaBoost + Haar features, PERCLOS drowsiness level | Works in all lighting
Eye Closeness (Raspberry Pi) [13] | Haar cascade + template matching on Pi | 99.59% accuracy
6

## Slide 7
Vehicular Parameter-Based Techniques
Detecting fatigue from driving behavior
• Real-time lane detection [16] Hough transform lane detection + Viola-Jones / Otsu / Canny eye detection; works in low light.
• Steering angular velocity [17] Time-series analysis of steering behavior with temporal detection window.
• Steering wheel angles (SWA) [18] Approximate Entropy (ApEn) features + piecewise fitting + warping distance classifier.
• SWA + Yaw angles (YA) [19] ApEn features + 2-6-6-3 back-propagation neural network; 3 fatigue levels.
Key Insight
A single steering angle sensor under the wheel detects steering reversals (0.5°–5°) during drowsiness. Limitations: • Affected by road geometry & weather • Grip force varies with mood & road type • Sometimes drowsiness doesn't change driving behavior
7

## Slide 8
Physiological Parameter-Based Techniques
Biological signals = highest reliability
Technique | Signals / Method | Result
EEG-based fatigue detection [20] | Single-electrode EEG, drowsiness-level index | Detects all tiredness levels
HRV + SVM classifier [21] | Wavelet analysis of heart-rate variability (PPG), ROC + SVM | 95% accuracy
Pulse sensor method [22] | Infrared pulse sensor on finger, LF/HF ratio | LF/HF drops when drowsy
Wearable wrist band [23] | PPG + galvanic skin response, 5 features + SVM | 98.02% accuracy
Wireless Bio-harness [24] | ECG, heart rate, posture via wearable biosensor | Mobile app alert
Driver fatigue system [25] | Somatic sensor: pulse, yawning, eye closure | Multi-stage alerts
ECG + EEG hybrid [26] | Time/frequency domain features, t-test selection, SVM | 80% with channel reduction
8

## Slide 9
Comparative Study of DDT
Pros, cons & performance under real conditions
Behavioral
Easy, non-intrusive. Cons: • Illumination effects • Reduced performance with sunglasses / mustache • Reduced in poor lighting
Vehicular
No body contact. Cons: • Dependent on weather & road geometry • Can be unreliable when behavior unchanged
Physiological
Most stable & accurate results. Cons: • Intrusive (electrodes on body) • Reduced accuracy with wireless / less contact
Trend: physiological measures are being made less intrusive via wireless sensors embedded in seats, seat belts, covers and steering wheels.
9

## Slide 10
Hybrid Approaches of DDT
Combining parameters to overcome individual limits
• Idea Combine physiological, behavioral and vehicular parameters so one technique reduces the limitations of another, increasing overall accuracy.
• ECG + EEG fusion [26] Combining heart (ECG) and brain (EEG) signals improves differentiation of drowsy vs. alert states - better than using either alone.
• Data fusion & robustness [31] Fusing multiple signals makes the system robust to signal loss.
• Smartphone-based fusion [29] Smartphone monitoring with data fusion of multiple sensors.
• Multi-modal feasibility [32] Multi-modal driver drowsiness detection feasibility study.
10

## Slide 11
Supervised Learning Classifiers
SVM, HMM and CNN - the three most used methods
SVM
Support Vector Machine - supervised learning for classification & regression. • Most widely used • Easy to use, fast • E.g., Haar face detection + SVM eye states
HMM
Hidden Markov Model - statistical model predicting hidden states from observed states. • Lowest error rate • Used for facial expressions, gene annotation, eye tracking
CNN
Convolutional Neural Network - layers of spatial convolution for images/video. • Best for image recognition • Handles changing head pose (3D CNN)
Insight: SVM gives good accuracy & speed in most situations but is not suitable for large datasets; CNN & HMM are slower and more expensive to train.
11

## Slide 12
Comparative Study of Classification
Trade-offs between accuracy, speed and cost
Accuracy
HMM has the lowest error rate, i.e., highest accuracy among the three classifiers.
Usability
SVM is easy to use and therefore the most commonly adopted classifier in drowsiness detection systems.
Cost & Speed
CNN and HMM are slow in training and expensive compared to SVM; SVM struggles with very large datasets.
Key takeaway: no single classifier fits every situation - choose based on system requirements for accuracy, speed and dataset size.
12

## Slide 13
Conclusion & Findings
State-of-the-art in drowsiness detection
• No perfect technique None of the detection techniques provides full accuracy alone.
• Physiological = most accurate Physiological parameters give the most accurate and stable results across conditions.
• Reduce intrusiveness Wireless sensors on the body, driving seat, seat belt, seat cover and steering wheel make physiological methods less intrusive.
• Hybrids win Combining techniques (e.g., ECG + EEG) improves performance over single methods.
• Classifier choice HMM is most accurate; SVM is easiest & most common; CNN excels at image-based detection - match the classifier to the task.
13

## Slide 14
References & Future Directions
Moving forward
Key Sources
IEEE Access paper DOI: 10.1109/ACCESS.2019.2914373 Survey of 41 primary studies from IEEE Xplore, ACM, Springer, Google Scholar, IJCS, MDPI covering behavioral, vehicular and physiological techniques (2015-2017 focus).
Future Work
• Less-intrusive physiological sensing (wearable + seat embedded) • Multi-modal / hybrid fusion systems • Real-time, low-cost embedded deployment • Robustness to lighting, glasses & road conditions • Scalable classifiers for large datasets
Thank you
14