## Slide 1
Drowsiness Detection for Driver Safety
First Review (Review 0) - Analysis of Survey Paper
Paper: "A Survey on State-of-the-Art Drowsiness Detection Techniques" Ramzan et al., IEEE Access, Vol. 7, 2019
Presented by: [Student Name] | Guide: [Guide Name]

## Slide 2
Presentation Outline
Agenda for Review 1
1. Introduction & Problem Statement
2. Objectives of the Study
3. Literature Review - Survey of Drowsiness Detection
4. Detection Techniques: Behavioral / Vehicular / Physiological
5. Comparative Analysis & Classification Methods
6. Research Gaps Identified
7. Proposed Work & Methodology
8. Expected Outcomes & Plan of Work
9. Conclusion & References
2

## Slide 3
Introduction & Problem Statement
Why driver drowsiness detection matters
Introduction
Drowsiness / fatigue is a major cause of road accidents. A continuous unconscious transition from wakefulness to sleep degrades driving performance and alertness. • NHTSA: ~100,000 accidents and 1,500+ deaths per year (US) • Drowsy drivers can be warned if detected in time • Modern vehicles can embed automatic fatigue detection systems
Problem Statement
Multiple detection techniques exist, each with benefits and limitations. There is no single method that provides full accuracy. • Behavioral: affected by illumination, glasses, mustache • Vehicular: unreliable in certain road/weather conditions • Physiological: accurate but intrusive Need: a comparative understanding and an improved approach to reliably detect drowsiness in real time.
3

## Slide 4
Objectives of the Study
What this work aims to achieve
R1. To systematically study and classify existing drowsiness detection techniques (behavioral, vehicular, physiological).
R2. To review and compare the top supervised learning classifiers used (SVM, HMM, CNN).
R3. To analyze the pros & cons and accuracy of each detection technique under real driving conditions.
R4. To identify research gaps and limitations in current drowsiness detection systems.
R5. To propose an improved / hybrid detection approach for better accuracy and driver safety.
4

## Slide 5
Literature Review - Survey Overview
Systematic review of 41 primary studies from 1,020 papers
Selection Process
1,020 papers searched (IEEE Xplore, ACM, Springer, Google Scholar, IJCS, MDPI) ↓ title relevance 105 papers ↓ abstract screening 74 papers ↓ full-text study 41 primary studies selected
What the Survey Covers
• Classifies techniques into 3 categories • Reviews each technique with novelty, features & limitations • Discusses hybrid approaches • Reviews supervised classifiers (SVM, HMM, CNN) • Presents pros/cons & comparative studies • Provides frameworks (diagrams) for understanding
5

## Slide 6
Technique 1: Behavioral Parameters
Non-invasive camera + computer vision
• Signals used Eye closure ratio (PERCLOS), eye blinking, head position, facial expressions, yawning.
• Eye Tracking + Dynamic Template Matching HSI model + Sobel edge operator for eyes - 99.01% accuracy.
• Mouth & Yawning Analysis SVM-trained mouth/yawning regions - outperforms geometric features.
• Yawning Extraction SVM face detection + Circular Hough Transform for wide-open mouth - 98% accuracy.
• Eye Closure + Head Postures Viola-Jones + Wavelet Network - 80% accuracy.
• Eye Blink Detection Blink rate below normal (12-19/min) triggers alert - 90% efficiency.
• Eye Closeness (Raspberry Pi) Haar cascade + template matching - 99.59% accuracy, all lighting, works with glasses.
Limitation
Accuracy is affected by illumination, brightness and road conditions; reduced performance with sunglasses or mustache.
6

## Slide 7
Technique 2: Vehicular Parameters
Detecting fatigue from driving behavior
• Signals used Lane-change patterns, vehicle speed variability, steering wheel angle, steering grip force.
• Real-time Lane Detection Hough transform for lanes + Viola-Jones / Otsu / Canny for eyes; works in low light.
• Steering Angular Velocity Time-series analysis with temporal detection window.
• Steering Wheel Angles (SWA) Approximate Entropy (ApEn) + linear piecewise fitting + warping distance - 78.01% accuracy.
• SWA + Yaw Angles ApEn features + 2-6-6-3 back-propagation NN - 88.02% average accuracy.
Limitation
Measurement easily affected by road geometry & weather; grip force depends on driver mood and road type; unreliable when drowsiness does not change driving behavior.
7

## Slide 8
Technique 3: Physiological Parameters
Biological signals - most accurate category
• Signals used Heart rate, pulse rate, breathing rate, body temperature, EEG / ECG / PPG / HRV.
• EEG-based Detection Single-electrode neuro-signal device; detects all levels of tiredness.
• HRV + SVM Wavelet analysis of heart-rate variability + SVM - 95% accuracy (vs 68.85% FFT).
• Pulse Sensor Infrared sensor on finger; LF/HF ratio decreases from awake to drowsy.
• Wearable Wrist Band PPG + galvanic skin response, 5 features + SVM - 98.02% accuracy.
• ECG + EEG Hybrid Combined features improve drowsy vs alert discrimination - 80% with channel reduction.
Limitation
Invasive - requires electrodes placed directly on the driver's body; can irritate the driver and is difficult to implement.
8

## Slide 9
Comparative Analysis of Techniques
Pros, cons and accuracy
Technique | Accuracy Examples | Advantages | Disadvantages
Behavioral | 80% - 99.59% | Non-invasive, camera-based, easy to use | Illumination / glasses / mustache effects
Vehicular | 78.01% - 88.02% | No body contact, uses vehicle sensors | Road geometry & weather dependent
Physiological | 80% - 98.02% | Most accurate & stable results | Intrusive; needs electrodes on body
Key finding: physiological parameters give the most accurate and stable results across lighting, sunglasses and mustache conditions. Their intrusiveness is being reduced via wireless sensors embedded in seats, seat belts, covers and steering wheels.
9

## Slide 10
Classification Methods (Supervised Learning)
SVM, HMM and CNN comparison
SVM
Support Vector Machine • Supervised learning for classification & regression • Easiest to use - most widely used in DDT • Good accuracy & speed in most situations • Not suitable for large datasets
HMM
Hidden Markov Model • Statistical model of hidden states from observed states • Lowest error rate (highest accuracy) • Used for facial expressions, eye tracking, wrinkle analysis • Slow & expensive training
CNN
Convolutional Neural Network • Spatial convolution layers - best for images/video • Representation learning for drowsiness detection • 3D CNN handles changing head pose • Slow & expensive training
Choosing the right classifier is critical - it directly impacts system efficiency and accuracy.
10

## Slide 11
Research Gaps Identified
Findings from the systematic review
• Accuracy: No single technique provides full accuracy - each category has limitations.
• Intrusiveness: Physiological methods are accurate but invasive; less-intrusive wireless versions lose accuracy.
• Environmental robustness: Behavioral methods degrade in poor lighting, with glasses / mustache; vehicular methods fail on poor roads.
• Real-time & cost: High-accuracy classifiers (HMM, CNN) are slow and expensive to train; SVM limited to small datasets.
• Single-modality limits: Individual signals alone are insufficient - combining signals improves performance.
11

## Slide 12
Proposed Work
Hybrid drowsiness detection system
Core Idea
Develop a hybrid driver drowsiness detection system that combines physiological signals (e.g., ECG / PPG) with behavioral features (eye closure, yawning) to overcome individual limitations and improve detection accuracy. • Leverage best accuracy of physiological measures • Reduce intrusiveness via wearable / non-contact sensors • Choose classifier by dataset size & real-time needs
Methodology Steps
1. Data acquisition (sensors / camera) 2. Preprocessing & feature extraction 3. Feature selection (statistical tests) 4. Classification (SVM / CNN) 5. Alert generation (multi-stage) 6. Performance evaluation (accuracy, sensitivity, specificity) 7. Comparison with survey benchmarks
12

## Slide 13
Expected Outcomes & Plan of Work
Roadmap for the project
Expected Outcomes
• An accurate hybrid drowsiness detection system • Real-time alerting for driver safety • Comparison and analysis vs. existing techniques (behavioral / vehicular / physiological) • Insights on optimal classifier selection • A documented framework for future work
Plan of Work
Phase 1: Literature review & gap analysis (Review 1) Phase 2: System design & dataset preparation (Review 2) Phase 3: Implementation of hybrid detection Phase 4: Testing & performance evaluation Phase 5: Results, analysis & documentation Phase 6: Final thesis / report submission
13

## Slide 14
Conclusion & References
Summary of the first review
Conclusion
The survey classifies drowsiness detection into behavioral, vehicular and physiological techniques. Physiological methods are most accurate, hybrids improve results, and classifier choice (SVM / HMM / CNN) must match the task. This review forms the basis for a proposed hybrid detection system for improved driver safety.
References
1. M. Ramzan et al., "A Survey on State-of-the-Art Drowsiness Detection Techniques," IEEE Access, vol. 7, pp. 61904-61919, 2019. DOI: 10.1109/ACCESS.2019.2914373 2. 41 primary studies surveyed across behavioral, vehicular and physiological techniques (IEEE Xplore, ACM, Springer, Google Scholar, IJCS, MDPI).
Thank you
14